## Slide 1: Computer Networks
Link State Routing
(§5.2.5, 5.6.6)

## Slide 2: Topic
How to compute shortest paths in a distributed network
  The Link-State (LS) approach
Flood!
… then compute

## Slide 3: Link-State Routing
One of two approaches to routing
  Trades more computation than distance vector for better dynamics
Widely used in practice
  Used in Internet/ARPANET from 1979
  Modern networks use OSPF and IS-IS

## Slide 4: Link-State Setting
Each node computes their forwarding table in the same distributed setting as distance vector:
Node knows only the cost to its neighbors; not the topology
Node can talk only to its neighbors using messages
Nodes run the same algorithm concurrently
Nodes/links may fail, messages may be lost

## Slide 5: Link-State Algorithm
Proceeds in two phases:
Nodes flood topology in the form of link state packets
  Each node learns full topology
Each node computes its own forwarding table
  By running Dijkstra (or equivalent)

## Slide 6: Phase 1: Topology Dissemination
Each node floods link state packet (LSP) that describes their portion of the topology
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Seq. # | 
A | 10
B | 4
C | 1
D | 2
F | 2
Node E’s LSP flooded to A, B, C, D, and F

## Slide 7: Phase 2: Route Computation
Each node has full topology
  By combining all LSPs
Each node simply runs Dijkstra
  Some replicated computation, but finds required routes directly
  Compile forwarding table from sink/source tree
  That’s it folks!

## Slide 8: Forwarding Table
To | Next
A | C
B | C
C | C
D | D
E | --
F | F
G | F
H | C
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Source Tree for E (from Dijkstra)
E’s Forwarding Table

## Slide 9: Handling Changes
On change, flood updated LSPs, and re-compute routes
  E.g., nodes adjacent to failed link or node initiate
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
XXXX
Seq. # | 
A | 4
C | 2
E | 4
F | 3
G | ∞
B’s LSP
Seq. # | 
B | 3
E | 2
G | ∞
F’s LSP
Failure!

## Slide 10: Handling Changes (2)
Link failure
  Both nodes notice, send updated LSPs
  Link is removed from topology
Node failure
  All neighbors notice a link has failed
  Failed node can’t update its own LSP
  But it is OK: all links to node removed

## Slide 11: Handling Changes (3)
Addition of a link or node
  Add LSP of new node to topology
  Old LSPs are updated with new link
Additions are the easy case …

## Slide 12: Link-State Complications
Things that can go wrong:
  Seq. number reaches max, or is corrupted
  Node crashes and loses seq. number
  Network partitions then heals
Strategy:
  Include age on LSPs and forget old information that is not refreshed
Much of the complexity is due to handling corner cases (as usual!)

## Slide 13: DV/LS Comparison
Goal | Distance Vector | Link-State
Correctness | Distributed Bellman-Ford | Replicated Dijkstra
Efficient paths | Approx. with shortest paths | Approx. with shortest paths
Fair paths | Approx. with shortest paths | Approx. with shortest paths
Fast convergence | Slow – many exchanges | Fast – flood and compute
Scalability | Excellent – storage/compute | Moderate – storage/compute

## Slide 14: IS-IS and OSPF Protocols
Widely used in large enterprise and ISP networks
  IS-IS = Intermediate System to Intermediate System
  OSPF = Open Shortest Path First
Link-state protocol with many added features
  E.g., “Areas” for scalability

## Slide 15: END
© 2013 D. Wetherall
Slide material from: TANENBAUM, ANDREW S.; WETHERALL, DAVID J., COMPUTER NETWORKS, 5th Edition, © 2011. Electronically reproduced by permission of Pearson Education, Inc., Upper Saddle River, New Jersey