## Slide 1
Chapter 2
Panvar
A Single Segment Network
– DDaattaa Link Layer
TCP/IP Essentials A Lab-Based Approach

## Slide 2: Data Link Layer
Main tasks of the data link layer:
TCP/IP Suite
–Transfer network layer data from one machine to another machine via “a data link”.
Application Layer
–Convert the data between raw bit stream of the physical layer and groups of bits  bytes
 frames.
Transport Layer
Network Layer
Data Link Layer
Physical Layer
–Perform flow control between sender and receiver
Error Detection and Correction
Sliding Window Protocols

## Slide 3: Types of Networks
Point-to-point network
Each link connects two end points: hosts or any network devices
Usually for long distance connections
Examples: DSL, POS (Packet over SONET/SDH), GbE (Gigabit Ethernet)
Broadcast network
A number of stations share a common transmission medium
Usually for local networks
Examples: CSMA/CD Ethernet, WLAN (Wireless Local Area Network), a.k.a. Wi-Fi
Broadcast Network
Point-to-Point Network

## Slide 4: Possible Services
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11
Acknowledged connection-oriented service
  Connection is set up; rare

## Slide 5: Multiple Access
•Network topology
–Point-to-point  N(N-1)/2 links to connect N nodes
–Broadcast  the shared medium forms a single domain
•Medium access control (MAC) protocols
–Rules to share a medium
–Carrier Sense Multiple Access/Collision Detection (CSMA/CD)
– Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA)

## Slide 6: Point-to-Point Protocol – point-to-point network example
The Point-to-Point Protocol (PPP) is a data link protocol
The main purpose of PPP is encapsulation and transmission of IP datagrams, or other network layer protocol data, over a serial link.
Currently, PPP is used by most dial-up Internet access, Digital Subscriber Loop (DSL), and cable broadband services.
DSL example
central office
telephone network
DSL
ISP
DSLAM
voice, data transmitted at different frequencies over dedicated line to central office
modem
splitter
DSL access multiplexer

## Slide 7: PPP Encapsulation
PPP frame format
• Flag: mark the beginning and ending of a frame
•Protocol: used to multiplex different protocol data
•No addressing, only two end hosts.
Flag
Addr.
Ctrl.
Protocol
Data
CRC
Flag
7E | FF | 03 |  |  |  | 7E
1 byte | 1 byte | 1 byte | 2 bytes | ≤ 1500 bytes | 2 bytes | 1 byte
 |  |  | 0021 | IP Datagram |  | 
 |  |  | C021 | Link Control Data |  | 
 |  |  | 8021 | Network Control Data |  | 

## Slide 8: Point-to-Point Protocol (RFC 1661)
PPP consists of two types of control protocols:
Link Control Protocol (LCP)
  Responsible for agreeing on PPP encapsulation options, packet size limits, and detecting common mis-configuration errors over the data link
  Optional features to provide peer authentication, detect link status
Network Control Protocol (NCP)
  PPP supports a family of NCPs and treat each network protocol like an interface
  IP Control Protocol (IPCP, RFC 1332), used for configure the link to transmit IP datagrams

## Slide 9: Packet over SONET
Packet over SONET is the method used to carry IP packets over SONET optical fiber links
  Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads

## Slide 10: ADSL (1)
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (over)

## Slide 11: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes
Notes: Re ATM: ATM was a major technology in the 1990s that was hyped to win in the convergence of the Internet and telecommunications, but IP won instead. The short, fixed-size cells give flexibility (can mix voice and data without having the voice wait for a whole data packet). ATM is now used in niches such as ADSL and WAN links.

## Slide 12: Why did Ethernet Win?
There are LOTS of LAN protocols
Price
Performance
Availability
Ease of use
Scalability
AT the time an Ethernet card costs $40, AN ATM card cost $1000

## Slide 13: PPP (2)
A link control protocol brings the PPP link up/down
State machine for link control

## Slide 14: Local Area Networks
Local Area Networks (LANs) typically connect computers within a building or a campus.
Many LANs are broadcast networks.
Bus and Ring are two typical LAN topologies used in early days
The protocol that determines who can transmit on a broadcast channel is called Medium Access Control (MAC) protocol.
Bus LAN
Ring LAN

## Slide 15: MAC and LLC
In any broadcast network, the stations must ensure that only one station transmits at a time on the shared communication channel.
The protocol that determines who can transmit on a broadcast channel is called Medium Access Control (MAC) protocol.
The MAC protocol is implemented in the
to Network Layer
MAC sublayer which is the lower sublayer
of the data link layer.
Logical Link Control
Data Link Layer
The higher portion of the data link layer
is often called Logical Link Control (LLC).
to Physical Layer
Medium Access
Control

## Slide 16: Logical Link Control
LLC can provide different services to the network layer:
  unacknowledged connectionless service
  acknowledged connectionless service
  connection-oriented service
Framing
Error control
Addressing

## Slide 17: Media Access Control
MAC algorithms are used to resolve collisions and share the medium in a broadcast network.
Examples of MAC:
ALOHA
Carrier Sense Multiple Access/Collision Detection (CSMA/CD)
Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA)
Ethernet
Originally developed at Xerox PARC at 2.94 Mbps data rate over coaxial cable based on CSMA/CD, 1972 – 1977
An industry standard since 1982 (DIX Ethernet), or
Based on CSMA/CD adopted by IEEE 802 committee in 1985
  Interoperates with 802.2 (LLC) as higher layer
  Uses different encapsulation header to carry data payload

## Slide 18: Collisions in Ethernet
The collision resolution process of Ethernet requires that a collision is detected while a station is still transmitting.
Assume the maximum propagation delay on the bus is a.
Restrictions: Each frame should be at least twice as long as the time to detect a collision (2a).
A Begins Transmission
A
B
t0
B Begins Transmission
A
B
t0+a- 
B Detects Collision
A
B
t0+a
A detects collision just before end of transmission
A
B
t0 +2a

## Slide 19: CSMA/CD Flow Diagram
1.Each station listens before it transmits.
2.If the channel is busy, it waits until the
Station has data to send
channel goes idle, and then it transmits.
3.If the channel is idle it transmits
Wait according to the backoff algorithm (5)
New Attempt
immediately and continue sensing for
2a seconds.
Sense Channel (1)
Channel Busy (2)
4.If collision is detected, transmit a brief jamming signal then cease transmission.
Transmit jam signal (4)
Transmit data and sense channel (3)
Collision Detected
Channel Free (2)
5. Wait for a random time, and retransmit. The random time is determined by
Complete
No Collision
exponential backoff algorithm.
Transmission

## Slide 20: Exponential Backoff Algorithm
•If a station is involved in a collision, it waits a random amount of time before attempting a retransmission.
•The random time is determined by the following algorithm:
–Set “slot time” to 2a.
–After first collision wait 0
or 1 time unit.
–After the ith collision, wait a random number between 0 and 2i-1 time slots.
– Do not increase random number range if i>9.
[G. Fairhurst]
– Give up after 16
collisions.

## Slide 21: Ethernet Switches
In an Ethernet LAN, hosts can be
Attached to a common cable, or
Connected by Ethernet switches.
A
B
C
Ethernet switches are MAC layer devices that switch frames between ports connected to different LAN segments.
Offer guaranteed bandwidth for segments.
Separate a LAN into collision domains.

## Slide 22: Ethernet Encapsulation (RFC 894)
.
IP
datagram
6
6
46-1500
Type 0800
2
4
2
46-1500
2
18
28
- Dest. Addr., Src. Addr.:
MAC addresses are 48 bit
28
18
2
- Type:
Identifies the content of the data field (must ≥ Ox0600)
cyclic redundancy check
- CRC:
Dest. Addr | Src. Addr. | Type | Data | CRC
Type 0806 | ARP req./reply | PAD
Type 8035 | RARP req./reply | PAD

## Slide 23: IEEE 802.2/802.3 Encapsulation
802.3 MAC
Destination address
Source address
Length
DSAP SSAP cntl Org code AA AA 03 0
type
Data
CRC
802.2 LLC
802.2 SNAP
6 6 2 1 1 1
- Destination address, Source address:
MAC addresses are 48 bit (displayed
3
2
38-1492
4
0800
IP datagram
as 12 hexadecimal characters)
frame length in number of bytes (<Ox0600, 1,500 bytes  Ox05dc)
- Length:
2
38-1492
0806
ARP request/reply
PAD
DSAP, SSAP:
Ctrl:
Org code:
Type field:
always set to set t o 3
set to 0
identifies the content of the
0xaa
2
28
10
8035
2
RARP request/reply PAD
28
10
Total frame size: 64 bytes to 1518 bytes
Overhead: 38 bytes including 12 bytes Inter Frame Gap (IFG)
data field
cyclic redundancy check
- CRC:

## Slide 24: The Address Resolution Protocol
IP addresses are not recognizable in the interface layer where physical addresses (or MAC addresses) are used.
Different kinds of physical networks use different addressing schemes.
Address Resolution Protocol (ARP): maps an IP address to a MAC address per RFC 826.
Reverse Address Resolution Protocol (RARP): maps a MAC address to an IP address per RFC 903.

## Slide 25: ARP Process
•When a source host wants to send an IP packet to a
destination, it first broadcasts an ARP request asking for the MAC address corresponding to a ttaarrggeett IIPP aaddddrreessss.
•A ttaarr ggeett ddeevviiccee will return an ARP reply with its MAC address.

## Slide 26: ARP Packet Format
28 bytes long.
An ARP request or ARP reply is encapsulated in an Ethernet frame.
– The protocol type in Ethernet frame is set to 0x0806 for ARP messages.
Hardware Type - Specifies a hardware interface type for which the sender requires a response, i.e. Ethernet (1) in our case
Protocol type - Specifies the type of high-level protocol address the sender has supplied, ie. IP (Ox0800) in our case
Hlen - Hardware address length.
Plen - Protocol address length.
Operation field specifies ARP request (1), ARP reply (2), RARP request (3), or RARP reply (4).

## Slide 27: ARP Request
Ethernet destination: ff:ff:ff:ff:ff:ff (broadcast address)
Target Ethernet Address: not set.

## Slide 28: ARP Reply
The ARP reply is sent by the node whose IP address matches the target IP address in the ARP request.
It fills its MAC address into the target Ethernet address field of the ARP request.
It then swaps the two sender addresses (Ethernet and IP addresses) with the two target addresses, sets the op field to 2.
The ARP reply is sent back to the source host only.
All other nodes receiving the broadcast ARP Request record the MAC and IP of the Sender

## Slide 29: ARP Cache
•Sending an ARP request/reply for each IP datagram is inefficient.
•Each host maintains an ARP cache containing the recent resolved IP addresses.
•A source host first checks its ARP cache for the destination MAC address,
If an entry is found, sends out the IP packet within an Ethernet frame.
Otherwise, sends out an ARP request.

## Slide 30: Manipulating the ARP Table
•Elements of an entry in the ARP table:
An IP address
A MAC address
Flags
•A normal entry expires after 20 minutes after it is created or the last time it is referred.
•Manipulate ARP table by the arp command:
arp –a: Displays all entries in the ARP table.
arp –d: Deletes an entry in the ARP table.
arp –s: Inserts an entry into the ARP table.

## Slide 31: Proxy ARP (RFC 1027)
Hide the two physical networks from each other.
A router answers ARP requests targeted for a host.
Physical Network 1
Physical Network 2
Note
Two networks are logically in the same subnet (at least from Host As point of view …)
Often used by a router connecting to a host with a serial link, ex. PPP to Host B
’

## Slide 32: Gratuitous ARP
Occurs when a host sends an ARP request resolving its own IP
address.
Usually happens when the interface is configured at bootstrap time.
The interface uses gratuitous ARP to determine if there are other hosts using the same IP address.
The sender’s IP and MAC address are broadcast, and other hosts will insert this mapping into their ARP tables.

## Slide 33: DHCP Function: High Level
Send My Configuration Information
Client
IP Address: 10.10.10.101 Subnet Mask: 255.255.255.0 Default Routers: 10.10.10.1 DNS Servers: 192.168.10.4, 192.168.10.5 Lease Time: 10 days
Here Is Your Configuration
DHCP Server
Server dynamically assigns IP address on demand
Administrator creates pools of addresses available for assignment
Address is assigned with lease time
DHCP delivers other configuration information in options

## Slide 34: DHCP Function: Lower Level
See: DHCP defined by RFC 2131
DHCP Server
Client
DHCP Discover (Broadcast)
DHCP Offer (Unicast|Broadcast)
DHCP Request (Broadcast)
DHCP Ack (Unicast|Broadcast)

## Slide 35: Loopback Interface
Most IP stack implementations have a loopback interface with IP address
127.0.0.1 and named as localhost.
The localhost behaves as a separate data link interface.
A packet that is sent to the loopback interface moves down the protocol stack and is returned back by the driver software for the localhost “device”.
Used for debugging.
Packets sent to loopback interface will not appear on network.

## Slide 36: Network Interface Operations
Functional Diagram of an Ethernet Interface Card

## Slide 37: Maximum Transmission Unit
There is a limit on the data packet size of each data link layer protocol.
This limit is called Maximum Transmission Unit (MTU).
MTUs for various data link layers:
  Ethernet, PPP: 1500 bytes
  FDDI: 4352 bytes
  PPP (low delay): 296 bytes
MTU does not count its own header and trailer bytes of the data link protocol. e.g. Ethernet’s MTU is 1500 bytes.
.
6
6
46-1500
2
4
Dest. Addr | Src. Addr. | Type | Data | CRC

## Slide 38: Internet Control Message Protocol
The Internet Control Message Protocol (ICMP) is the protocol used for error and control messages in Internet.
ICMP provides an error reporting mechanism of routers to the sources.
All ICMP packets are encapsulated as IP datagrams (IP protocol type 1)
The packet format is simple.
Example below shows destination unreachable error message below:

## Slide 39
Types of ICMP Packets
Many ICMP packet types exist, each with its own format.

## Slide 40: ICMP Message Types
ICMP messages are either query messages or error messages.
ICMP query messages:
  Echo request / Echo reply
  Router advertisement / Router solicitation
  Timestamp request / Timestamp reply
  Address mask request / Address mask reply
ICMP error messages:
  Host unreachable
  Source quench
  Time exceeded
  Parameter problem

## Slide 41: ICMP Error Messages
Each ICMP error message contains the header and at least the first 8 bytes of the IP datagram payload that triggered the error message.
To prevent that too many ICMP messages, ICMP error messages are NOT sent
  for multiple fragments of the same IP datagrams
  in response to an error message
  in response to a broadcast packet

## Slide 42: ICMP Type 3 Error Message Code
There are 16 different ICMP error messages (‘codes’) of type “Destination Unreachable” (Type = 3)
Code Message Type
0 Network unreachable
Host unreachable
Protocol unreachable
Port unreachable
Fragmentation needed but bit not set Source route failed
Code Message Type
Source host isolated
Destination network administratively prohibited Destination host administratively prohibited Network unreachable for TOS Host unreachable for TOS
5
10
1
12
6
Destination network unknown
Destination node unknown
7
13
Communication administra- tively prohibited by filtering Host precedence violation
14
15
Precedence cutoff in effect

## Slide 43: ICMP Port Unreachable
If, in the destination host, the IP module cannot deliver the datagram because the indicated protocol module or process port is not active, the destination host may send a port unreachable message to the source host.
Client
Server
No process is waiting at Port 1234

## Slide 44: ICMP Port Unreachable
Format of the Port Unreachable Message
ICMP Message
Ethernet Header
IP Header
ICMP
Header
IP header of datagram from client
at least 8 bytes from IP payload of client
Type (= 3)
Code (= 3)
Checksum
8 bytes
Unused (Set to 00...0)
Note: both UDP and TCP store the
Port Number in the first 8 bytes!

## Slide 45: Packet InterNet Gopher (PING)
PING is a program that utilizes the ICMP echo request and echo reply messages.
PING is used to verify if a certain host is up and running. It is used extensively for fault isolation in IP networks.
PING can be used with a wide variety of options, e.g.
  -R (Record route): includes the RECORD_ROUTE option in the ECHO_REQUEST packet and displays the route buffer on returned packets.
  -s packetsize: specifies the number of data bytes to be sent (default is 56) (in newer implementations, -s is used to continuously generate queries)

## Slide 46: Echo Request and Reply
Ping’s are handled directly by the kernel.
Each Ping is translated into an ICMP Echo Request.
The Ping’ed host responds with an ICMP Echo Reply.
Host 1
Host 2
Message format
  Identifier is set to process ID of querying process.
  Sequence number is incremented for each new echo request.

## Slide 47: Sock Traffic Generator
Sock is a test program.
  Can be run as a client or as a server
  Use UDP or TCP.
Sock
Server
stdin
TCP Connection
stdout
Sock operates in one of the following four modes:
  Interactive client
> Copy data from stdin, send to server, receive data back from server, copy on screen (stdout)
  Interactive server
> Wait for a request from client
  Source client
> Send packets to a specific server
  Sink server
> Receive packets from a client and discard the data