## Slide 1: MAC Address CAM Table
CAM table stands for Content Addressable Memory
The CAM tables stores information such as MAC addresses available on physical ports with their associated VLAN parameters
All CAM tables have a fixed size
0000.0cXX.XXXX
48-Bit Hexadecimal Number Creates Unique Layer Two Address
1234.5678.9ABC
First 24-Bits = Manufacture Code Assigned by IEEE
Second 24-Bits = Specific Interface, Assigned by Manufacture
0000.0cXX.XXXX
All Fs = Broadcast
FFFF.FFFF.FFFF

## Slide 2: Normal CAM Behavior 1/3
MAC A
Port 1
Port 2
Port 3
MAC Port
A 1
C 3
ARP for B
ARP for B
ARP for B
B Is Unknown— Flood the Frame
MAC B
MAC C

## Slide 3: Normal CAM Behavior 2/3
MAC A
Port 1
Port 2
Port 3
MAC Port
A 1
C 3
A is on Port 1
LEARN
B is on Port 2
MAC B
MAC C
B 2
I Am MAC B
I Am MAC B

## Slide 4: Normal CAM Behavior 3/3
MAC A
Port 1
Port 2
Port 3
MAC Port
A 1
C 3
Traffic A -> B
Traffic A-> B
B Is on Port 2
MAC B
MAC C
Does Not See Traffic to B
B 2

## Slide 5: CAM Overflow
I Am MAC Y
MAC A
MAC B
MAC C
Port 1
Port 2
Port 3
MAC Port
A 1
B 2
C 3
Y Is on Port 3
Z Is on Port 3
Y 3
Traffic A  B
I See Traffic to B
Assume CAM Table Now Full
I Am MAC Z
Traffic A  B
Traffic A  B

## Slide 6: CAM Table FULL
Once the CAM table on the switch is full, traffic without a CAM entry is flooded out every port on that VLAN
This will turn a VLAN on a switch into a “hub”
This attack will also fill the CAM tables of adjacent switches
10.1.1.22 -> (broadcast) ARP C Who is 10.1.1.1, 10.1.1.1 ?
10.1.1.22 -> (broadcast) ARP C Who is 10.1.1.19, 10.1.1.19 ?
10.1.1.26 -> 10.1.1.25 ICMP Echo request (ID: 256 Sequence number: 7424)  OOPS
10.1.1.25 -> 10.1.1.26 ICMP Echo reply (ID: 256 Sequence number: 7424)  OOPS